## Slide 1: ESD LAB CODES

## Slide 2: Program 1: Blinking LED
#include <stm32f4xx.h>
int main(void) {
RCC->AHB1ENR |= RCC_AHB1ENR_GPIODEN; // Enable GPIO D clock
GPIOD->MODER |= GPIO_MODER_MODER12_0; // Set pin 12 as output
while(1) {
GPIOD->ODR ^= GPIO_ODR_ODR_12; // Toggle pin 12
for(int i = 0; i < 1000000; i++); // Delay
}
}

## Slide 3: Program 2: Reading GPIO Input
#include <stm32f4xx.h>
int main(void) {
RCC->AHB1ENR |= RCC_AHB1ENR_GPIOAEN; // Enable GPIO A clock
GPIOA->MODER &= ~GPIO_MODER_MODER0; // Set pin 0 as input
while(1) {
if(GPIOA->IDR & GPIO_IDR_IDR_0) {
// Pin 0 is high
}
else {
// Pin 0 is low
}
}
}

## Slide 4: Program 3: PWM Output
#include <stm32f4xx.h>
int main(void) {
RCC->AHB1ENR |= RCC_AHB1ENR_GPIODEN; // Enable GPIO D clock
RCC->APB1ENR |= RCC_APB1ENR_TIM4EN; // Enable TIM4 clock
GPIOD->MODER |= GPIO_MODER_MODER12_1; // Set pin 12 as AF mode
GPIOD->AFR[1] |= 0x2 << ((12-8)*4); // Set pin 12 to AF2 (TIM4)
TIM4->PSC = 83; // Set prescaler
TIM4->ARR = 999; // Set auto-reload value
TIM4->CCMR1 |= TIM_CCMR1_OC1M_2 | TIM_CCMR1_OC1M_1; // PWM mode 1
TIM4->CCR1 = 500; // Set duty cycle
TIM4->CCER |= TIM_CCER_CC1E; // Enable output
TIM4->CR1 |= TIM_CR1_CEN; // Enable timer
while(1) {
// Code here
}
}

## Slide 5: Program 4: UART Communication
#include <stm32f4xx.h>
void UART_Init() {
RCC->AHB1ENR |= RCC_AHB1ENR_GPIOAEN; // Enable GPIO A clock
RCC->APB2ENR |= RCC_APB2ENR_USART1EN; // Enable USART1 clock
GPIOA->MODER |= GPIO_MODER_MODER9_1 | GPIO_MODER_MODER10_1; // Set pins 9 and 10 as AF mode
GPIOA->AFR[1] |= 0x7 << ((9-8)*4) | 0x7 << ((10-8)*4); // Set pins 9 and 10 to AF7 (USART1)
USART1->BRR = 0x16D; // Set baud rate to 9600
USART1->CR1 |= USART_CR1_TE | USART_CR1_RE | USART_CR1_UE; // Enable transmitter, receiver, and USART
}
void UART_SendChar(char c) {
while(!(USART1->SR & USART_SR_TXE)); // Wait for TX buffer to be empty
USART1->DR = c; // Send character
}
char UART_ReceiveChar() {
while(!(USART1->SR & USART_SR_RXNE)); // Wait for data to be received
return USART1->DR; // Read received data
}
int main(void) {
UART_Init();
while(1) {
char received = UART_ReceiveChar();
UART_SendChar(received); // Echo back received character
}
}

## Slide 6: Program 5: Timer Interrupt
#include <stm32f4xx.h>
void TIM2_IRQHandler() {
TIM2->SR &= ~TIM_SR_UIF; // Clear update interrupt flag
// Code to be executed on timer interrupt
}
int main(void) {
RCC->APB1ENR |= RCC_APB1ENR_TIM2EN; // Enable TIM2 clock
TIM2->PSC = 83; // Set prescaler
TIM2->ARR = 9999; // Set auto-reload value (10ms)
TIM2->DIER |= TIM_DIER_UIE; // Enable update interrupt
NVIC_EnableIRQ(TIM2_IRQn); // Enable TIM2 interrupt in NVIC
TIM2->CR1 |= TIM_CR1_CEN; // Enable timer
while(1) {
// Code here
}
}

## Slide 7: Program 6: ADC Reading
#include <stm32f4xx.h>
void ADC_Init() {
RCC->AHB1ENR |= RCC_AHB1ENR_GPIOAEN; // Enable GPIO A clock
RCC->APB2ENR |= RCC_APB2ENR_ADC1EN; // Enable ADC1 clock
GPIOA->MODER |= GPIO_MODER_MODER0; // Set pin A0 as analog mode
ADC1->CR2 |= ADC_CR2_ADON; // Enable ADC
ADC1->CR2 |= ADC_CR2_SWSTART; // Start conversion
}
uint16_t ADC_Read() {
while(!(ADC1->SR & ADC_SR_EOC)); // Wait for conversion to complete
return ADC1->DR; // Read result
}
int main(void) {
ADC_Init();
while(1) {
uint16_t result = ADC_Read();
// Process ADC value
}
}

## Slide 8: Program 7: I2C Communication
#include <stm32f4xx.h>
void I2C_Init() {
RCC->AHB1ENR |= RCC_AHB1ENR_GPIOBEN; // Enable GPIO B clock
RCC->APB1ENR |= RCC_APB1ENR_I2C1EN; // Enable I2C1 clock
GPIOB->MODER |= GPIO_MODER_MODER6_1 | GPIO_MODER_MODER7_1; // Set pins 6 and 7 as AF mode
GPIOB->AFR[0] |= 0x4 << (6*4) | 0x4 << (7*4); // Set pins 6 and 7 to AF4 (I2C1)
I2C1->CR2 |= 0x8; // Set peripheral clock to 8MHz
I2C1->CCR |= 0x28D; // Set clock control register (calculated for 100kHz)
I2C1->TRISE |= 0x9; // Set rise time register (calculated for 100kHz)
I2C1->CR1 |= I2C_CR1_PE; // Enable I2C
// Master initialization complete
}
void I2C_Write(uint8_t address, uint8_t data) {
I2C1->CR1 |= I2C_CR1_START; // Generate START condition
while(!(I2C1->SR1 & I2C_SR1_SB)); // Wait for start condition to be generated
I2C1->DR = (address << 1) & 0xFE; // Send slave address (write mode)
while(!(I2C1->SR1 & I2C_SR1_ADDR)); // Wait for address to be sent
while(!(I2C1->SR2 & I2C_SR2_TRA)); // Wait for transmit mode
I2C1->DR = data; // Send data byte
while(!(I2C1->SR1 & I2C_SR1_BTF)); // Wait for byte transfer finished
I2C1->CR1 |= I2C_CR1_STOP; // Generate STOP condition
}
int main(void) {
I2C_Init();
while(1) {
I2C_Write(0x50, 0x12); // Write 0x12 to slave with address 0x50
}
}

## Slide 9: Program 8: External Interrupt
#include <stm32f4xx.h>
void EXTI0_IRQHandler() {
if(EXTI->PR & EXTI_PR_PR0) {
EXTI->PR |= EXTI_PR_PR0; // Clear interrupt flag
// Code to be executed on EXTI0 interrupt
}
}
void EXTI_Init() {
RCC->AHB1ENR |= RCC_AHB1ENR_GPIOAEN; // Enable GPIO A clock
RCC->APB2ENR |= RCC_APB2ENR_SYSCFGEN; // Enable SYSCFG clock
GPIOA->MODER &= ~GPIO_MODER_MODER0; // Set pin 0 as input
SYSCFG->EXTICR[0] |= SYSCFG_EXTICR1_EXTI0_PA; // Connect EXTI0 to PA0
EXTI->IMR |= EXTI_IMR_MR0; // Enable EXTI0 interrupt
EXTI->FTSR |= EXTI_FTSR_FT0; // Set falling edge trigger
NVIC_EnableIRQ(EXTI0_IRQn); // Enable EXTI0 interrupt in NVIC
}
int main(void) {
EXTI_Init();
while(1) {
// Code here
}
}

## Slide 10: Program 9: PWM Output (Alternate Timer)
#include <stm32f4xx.h>
int main(void) {
RCC->AHB1ENR |= RCC_AHB1ENR_GPIODEN; // Enable GPIO D clock
RCC->APB1ENR |= RCC_APB1ENR_TIM3EN; // Enable TIM3 clock
GPIOD->MODER |= GPIO_MODER_MODER12_1; // Set pin 12 as AF mode
GPIOD->AFR[1] |= 0x2 << ((12-8)*4); // Set pin 12 to AF2 (TIM3)
TIM3->PSC = 83; // Set prescaler
TIM3->ARR = 999; // Set auto-reload value
TIM3->CCMR1 |= TIM_CCMR1_OC1M_2 | TIM_CCMR1_OC1M_1; // PWM mode 1
TIM3->CCR1 = 500; // Set duty cycle
TIM3->CCER |= TIM_CCER_CC1E; // Enable output
TIM3->CR1 |= TIM_CR1_CEN; // Enable timer
while(1) {
// Code here
}
}

## Slide 11: Program 10: Software Delay
#include <stm32f4xx.h>
void delay_ms(uint32_t ms) {
volatile uint32_t i = 0;
for(i = 0; i < ms * 12000; i++);
}
int main(void) {
RCC->AHB1ENR |= RCC_AHB1ENR_GPIODEN; // Enable GPIO D clock
GPIOD->MODER |= GPIO_MODER_MODER12_0; // Set pin 12 as output
while(1) {
GPIOD->ODR ^= GPIO_ODR_ODR_12; // Toggle pin 12
delay_ms(500); // Delay for 500 ms
}
}